## Slide 1
How to Identify
Genuine BMW Parts
A Complete Guide for BMW Owners & Mechanics
Notes: A complete guide to identifying genuine BMW parts — covering part types, part numbers, verification methods, common fakes, and MOT rules.

## Slide 2
The Four Types of BMW Replacement Parts
Understanding what you are buying matters before any parts purchase. These four categories have different quality, price, and risk profiles.
GENUINE
BMW-branded, dealer-supplied
• Made by or for BMW AG
• Carries official BMW branding and packaging
• Same part used on the production line
• Highest price, full retail supply chain
Highest price
OEM
Same factory, no BMW badge
• Manufactured by the same supplier BMW uses
• Identical specification, no BMW branding
• Often 30–50% cheaper than genuine
• The most common alternative for specialists
Best value
AFTERMARKET
Third-party manufacturer
• Produced by unrelated third-party companies
• Quality varies enormously between brands
• Some match OEM spec, many do not
• Lowest price, highest quality risk
Variable quality
USED
Removed from a donor vehicle
• Original genuine or OEM part, second-hand
• Tested, graded, sold with donor mileage
• Fraction of new or OEM pricing
• Best value for out-of-warranty cars
Smart choice
Notes: Genuine = BMW-branded. OEM = same manufacturer, no badge. Aftermarket = unrelated third party. Reclaimed = original part removed from a written-off or end-of-life donor vehicle, tested and resold.

## Slide 3
Understanding the BMW Part Number System
Every genuine BMW part has an 11-character OEM number. Knowing how to read it is the most reliable way to verify any listing.
11 12 7 625 809
11
Main Group
Two-digit code identifying the
major system the part belongs to.
01 = Engine internals
11 = Engine block
18 = Exhaust system
51 = Body / exterior
63 = Lighting
12
Sub-Group
Two-digit code for the specific
component category within the
main group.
Narrows the part down to a
specific assembly or function
within that system.
7 625 809
Part Identifier + Check Digit
Seven characters identifying the
exact part within that sub-group.
The final digit is a check digit —
a mathematical verification that
the preceding numbers are
correct and complete.
Notes: BMW part numbers follow a consistent 11-character format. Use RealOEM.com with your VIN to find the correct number for any part on your specific car. Cross-referencing the number on any listing against your VIN lookup is the single most reliable verification step available.

## Slide 4
Where to Find and Verify a BMW Part Number
01
RealOEM.com – VIN-Based Catalogue
The most reliable free resource. Enter your 17-character VIN to access the factory parts catalogue for your specific car, including production date, options, engine code and body style. Confirms the correct part number for your exact specification, not just the model and year.
02
Stamped or Moulded on the Part Itself
Most genuine BMW parts have the OEM part number stamped, moulded, or laser-etched directly onto the housing, casing, or mounting surface. On sensors and electronic modules it is typically on a label attached to the unit.
03
Original BMW Packaging Label
New genuine parts come in a box carrying the BMW parts group label, which includes the full 11-character part number in the format XX XX X XXX XXX, a barcode, and the component description.
04
Previous Service Invoices
A BMW dealer or specialist invoice records the part numbers of everything replaced during a service or repair. Useful for cross-referencing what is currently fitted to the car and what standard part it came from.
Notes: RealOEM.com is free and widely used by BMW specialists and independent mechanics. Always use VIN rather than model/year — BMW changes part specifications mid-production without changing the external badge.

## Slide 5
Why the VIN Matters More Than Model and Year
The Problem
Searching by model and year alone
• BMW frequently updates components mid-production without changing the external model badge
• Two cars of the same model and year can require completely different headlights, sensors, or trim
• Pre-LCI and post-LCI (facelift) cars share a model name but have different parts from bumper to sensor
• "BMW 3 Series 2019" could be an F30 produced in early 2019 or a G20 launched later that year
• Engine code variants within the same model year can require different mechanical parts
The Solution
Use the 17-character VIN
Found on:
Windscreen base, Door jamb sticker, V5C document
Encodes:
Exact model, Production date, Engine code, Drivetrain, Body style, Factory options
Use at:
RealOEM.com – free, instant, accurate for any BMW from any production date
Tells you:
The exact OEM part number for every component on your specific car
Gives you:
The ability to verify any listing before purchase with a single cross-reference
Notes: The VIN is the only identifier that resolves all mid-production specification changes. RealOEM.com is free and widely trusted by BMW specialists worldwide.

## Slide 6
Red Flags: Signs a BMW Part May Not Be Genuine
Counterfeit BMW parts circulate through online marketplaces. Safety-critical fakes including airbag inflators and brake components have been documented by trading standards. These signals apply to any listing.
⚠ Price dramatically below all other listings
A genuine BMW part priced 60–80% below every comparable listing is a warning sign, not a bargain. Counterfeits are priced to attract buyers who search for the lowest figure.
⚠ Stock photo instead of the actual part
Any listing using a generic stock image rather than a photograph of the specific part on offer cannot confirm what will actually be shipped. Always request a real photo of the item.
⚠ No OEM part number stated
A seller who cannot or will not state the 11-character OEM part number has not confirmed what they are selling. A genuine seller of genuine parts will always know and state the number.
⚠ Packaging errors or branding inconsistencies
Counterfeit parts often have subtle misprints, incorrect font weights, or colour discrepancies in the BMW parts label. Compare carefully against known genuine packaging imagery.
⚠ No warranty offered on a significant component
Any reputable supplier of genuine parts backs them with a minimum warranty period. No warranty at all is itself a signal about the seller's confidence in the item.
⚠ No donor vehicle mileage for a used part
"Low mileage" without a specific figure is not a specification. A genuine used parts specialist will state the actual odometer reading of the donor vehicle as a confirmed number.
Notes: Trading Standards and consumer groups have documented counterfeit airbag inflators, brake pads, and steering components in the UK used parts market. The consequences of safety-critical fakes go well beyond a wasted purchase.

## Slide 7
Verification Checklist Before Buying Any BMW Part
Apply this checklist to any purchase – new dealer part, used genuine, or aftermarket. Each step removes a common failure mode.
✓
OEM part number confirmed
Matches the number from your VIN-based catalogue lookup at RealOEM.com
✓
Fitment verified against your VIN
Not just model and year, your specific production date and specification
✓
Donor mileage stated (used parts)
Actual odometer reading from the donor vehicle, not an estimate or "low mileage"
✓
Generation, body style, and build date match
Pre/post-facelift, saloon vs touring, drivetrain (RWD vs xDrive) confirmed
✓
Actual photographs of the part provided
Real photos of the specific item, not stock imagery
✓
Warranty terms stated in writing
Minimum 30 days for any significant component; confirm what the warranty covers
✓
Payment method offers buyer protection
PayPal Goods & Services or platform checkout, not bank transfer or cash
Notes: This checklist applies equally to purchases from marketplaces, breakers yards, independent specialists, and dealer parts departments. The steps that matter most: OEM number and VIN confirmation. The steps most often skipped: donor mileage and payment protection.

## Slide 8
Genuine BMW Parts, the MOT, and Type Approval
Does the MOT require new or dealer parts?
No. The DVSA MOT inspection manual tests whether a component functions correctly and meets the required standard at the time of inspection. It does not require parts to be new, dealer-supplied, or BMW-branded. A used genuine part that is correctly fitted and in serviceable condition is assessed on exactly the same basis as a new dealer part.
What is type approval and which parts need it?
Certain safety-critical parts must carry E-mark type approval to be legally fitted to a road vehicle in the UK. These include headlamps, windscreens, tyres, catalytic converters, diesel particulate filters, and brake components. Original BMW parts, new or used, were manufactured to type approval standards and retain the E-mark. Aftermarket replacements must independently carry the correct approval mark.
The emissions equipment rule
Under the DVSA MOT inspection manual, vehicles first used after 1 September 2002 must be rejected where original emissions control equipment (catalytic converter, DPF, EGR) is missing, obviously modified, or obviously defective. A decat pipe or DPF delete is an automatic MOT fail regardless of the actual emissions test reading. A genuine used catalytic converter or DPF meets this requirement identically to a new dealer part.
Manufacturer warranty: a separate matter
A BMW manufacturer warranty is a commercial agreement between BMW AG and the buyer. It is entirely separate from the MOT, which is a statutory roadworthiness test administered by DVSA. The source of a fitted part, dealer, specialist, or used, has no bearing on whether a car passes or fails the MOT.
Notes: Source for all claims on this slide: DVSA MOT Inspection Manual (current edition). The emissions equipment rule is the only area in the MOT that comes close to specifying parts content — and used genuine parts satisfy it identically to new dealer parts.

## Slide 9
How Reputable Breakers Yards Work in the UK
A licensed BMW breakers yard operating under UK End-of-Life Vehicle Regulations provides a documented, legal supply chain for used genuine parts. Understanding the process helps you assess any supplier.
01
ATF Certification
Any business dismantling vehicles in the UK must be an Authorised Treatment Facility (ATF), regulated by the Environment Agency (England/Wales), SEPA (Scotland), or DAERA (Northern Ireland). Verify via the relevant public register before purchasing.
02
Depollution First
Before any parts are removed, the vehicle must be depolluted, fuel, oil, coolant, brake fluid, refrigerant, airbag pyrotechnics, and the battery must all be safely removed. Until this step is complete, the vehicle is classified as hazardous waste under law.
03
Parts Assessment and Grading
Components are removed, cleaned, tested where appropriate, and graded by condition. A quality specialist records the donor vehicle's VIN and mileage against each part, giving buyers traceable provenance and enabling fitment confirmation.
04
Certificate of Destruction
Once fully processed, the ATF issues a Certificate of Destruction (CoD) to the DVLA, formally deregistering the vehicle. This is a legal requirement, and an ATF that cannot issue a CoD is not operating correctly.
Notes: ATF registers: Environment Agency (England/Wales), SEPA (Scotland), DAERA (Northern Ireland). A specialist BMW breakers yard that checks parts against VINs, confirms donor mileage, and provides a warranty is operating at a significantly higher standard than the bare legal minimum.

## Slide 10
MT Auto Parts
BMW Breakers Yard, Thurnscoe, South Yorkshire, ATF Permit GB3106UW/A001
15,000+
Five-star
reviews
F, G, U
BMW generations
2012 onwards
30-day
Warranty on
almost all parts
24–48hr
UK mainland
delivery
What we stock
Engines, Gearboxes, Alloy Wheels, Lighting, Body Parts, Interior Trim, Drivetrain & Suspension, Electronics, Brakes, Exhaust Systems, Restraint Systems
Free delivery on parts under 20 kg. VIN confirmation before dispatch, WhatsApp enquiries welcome
mtautoparts.com
Notes: MT Auto Parts is a family-run BMW specialist breakers yard in Thurnscoe, South Yorkshire, operated by Maxis Trading Ltd. All parts from F, G and U-generation BMWs from 2012 onwards, dismantled under ATF permit GB3106UW/A001.

## Slide 11
Key Takeaways
There are four part types
Genuine, OEM, aftermarket, and used. Each has different quality, price, and risk. Used genuine is often the best value for out-of-warranty cars.
Part numbers are the foundation
The 11-character OEM number, cross-referenced against your VIN at RealOEM.com, is the most reliable verification step available.
VIN beats model and year
BMW changes components mid-production. Your VIN identifies your exact specification, use it every time.
Six consistent red flags
Price too low, no real photo, no part number, packaging errors, no warranty, no donor mileage. Any one of these warrants caution.
MOT tests function, not origin
A correctly fitted, serviceable used genuine part meets the same MOT standard as a new dealer part. The DVSA does not require parts to be new.
ATF certification = legal provenance
A licensed breakers yard depollutes vehicles legally, records provenance, and issues Certificates of Destruction. Verify ATF status before purchasing.
How to Identify Genuine BMW Parts: A Complete Guide
Notes: Six key takeaways covering part types, part number system, VIN importance, red flags, MOT rules, and breakers yard licensing.